## Slide 1: Advanced Design Methods (MDO, KBE) AE4233
Introduction to Response Surface Models optimization
Dr.ir. G. La Rocca
Dr.ir. H.A. Visser
Ir. D. Steenhuizen
Dr. A. Elham
Flight Performance & Propulsion Group (FPP)

## Slide 2: What’s the problem here?
For a simple problem with a few des var, the optimization algorithm might need 20-50 workflow evaluations
One workflow evaluation can take up to 25 minutes
Notes: Assume you have built the analysis tool workflow shown above in the slide, where various tools are connected to perform MDO.
You made use of methods of relatively low fidelity in the hope to get a quick optimization.
Still you want to obtain relatively accurate results, that is why you have mixed class I methods with other simulation tools, such a VLM method for aerodynamic calculation and some other simulation tool you developed yourself.
You find out that to run a complete evaluation of the workflow (without optimization) it takes about 25 minutes, because some internal convergence loops are required (for example for mass convergence).
In case you want to use this workflow, even for a simple optimization problem with a couple of design variables, you can expect something like 20-50 evaluations by the optimizer. However, that means you need at least 20 hours of computation!
Well, can you do something about that??

## Slide 3: Surrogate modeling approach
A possible approach to avoid computing lengthy simulations for each objective evaluation is to build some approximation models of the system to be analysed.
These approximation models are the so called surrogate models (or response surface models, or metamodels or emulators).
These approximation models must mimic (i.e. predict) the behavior of the actual simulations as accurately as possible, while being computationally inexpensive to evaluate.

## Slide 4: Surrogate modeling approach
The idea is to use a limited number of function evaluations (by running the complete workflow with all its simulations) and use them to build a predictor function (i.e., the surrogate model)
Then the actual optimization will be performed evaluating the predictor function and NOT by running the full simulations.
In this way, the MDO problem is transformed and simplified into the optimum search of an analytical function
Also, the surrogate model can give insight in the relation between independent variables and response
Notes:   Interpolating
  Non-interpolating

## Slide 5: Optimization using RSM
Selection of sample points in the design space
Perform Design of Experiments (DoE) to find the response corresponding to the chosen sample points (using the full simulation workflow)
Build a Response Surface Model (RSM) with the results obtained at 2
Perform the optimization on the RSM obtained at point 3
Update the RSM, including as new sample point the design vector corresponding to the optimum found at 4 (i.e. a new experiment is generated using the full simulation workflow)
Re-perform the optimization with the updated RSM
If one of the two following convergence checks fails, go back to 5
  Conv. criteria on the optimum (is it really an optimum?)
  Conv. criteria on the optimum evaluated on RSM and the one computed using the full simulation workflow
Notes: Note that quite often, in literature, the selection of the sample points is considered as part of the DOE process, not a separate step as indicated above.
It is clear that, in order to update the RSM, the full workflow (with all its simulations) must be run again, every time the optimizer has found a potential optimum.
However, this is still much more efficient that evaluating the full workflow at each evaluation performed by the optimizer (to get to the optimum)

## Slide 6: Optimization using RSM Design of Experiments
1. Choose data / sample points
Example of Latin Hyper-cube sampling for two des.var.
How to choose the points on which to evaluate the system response to create the response surface?
  The idea is to get the most information with the least amount of effort, i.e. the least amount of evaluations
X1
X2
Notes: The first step is to choose a set of sample points at which the workflow will be evaluated.

## Slide 7: Optimization using RSM Design of Experiments
1. Choose data / sample points
Example of a maximin Latin square (a version of Latin Hyper-cube)
How to choose the points on which to evaluate the system response to create the response surface?
  The idea is to get the most information with the least amount of effort, i.e. the least amount of evaluations
X1
X2
Notes: The first step is to choose a set of sample points at which the workflow will be evaluated.

## Slide 8: Optimization using RSM Design of Experiments
2. Evaluate the model at the chosen sample points (Design of Experiments)
Sample points
Experiments
Actually you do not know this!!!
Notes: In the next step the workflow is evaluated at these sample points. This is called a Design of Experiments.
In the picture you can see the points over here are the sample points, and these points are the responses of the model.

## Slide 9: Optimization using RSM
3. Build the Response Surface Model (RSM)
Notes: After that a Response Surface Model is created of these results. Different methods exists to interpolate or fit the experiments and generate the response surface. For the specific example above the Kriging method was used.

## Slide 10
Interpolating methods increase in accuracy as the number of points increases
Non-Interpolating have good characteristics with respect to noise in the data
fit
interpolating
An example of response surface can be a polynomial model, where the original model is approximated by a polynomial function. More complex approximation forms exist.
Optimization using RSM Interpolating vs non-interpolating

## Slide 11
Least Squares method (non-interpolating)
Note; x can consist of measured values or non-dimensionalized and centered variables
Optimization using RSM
Building surrogates with LSM approach

## Slide 12: Response surface (LSM) example

## Slide 13: Response surface (LSM) example

## Slide 14: Response surface (LSM) example

## Slide 15: Response surface (LSM) example

## Slide 16: Optimization using RSM Building surrogates with Kriging
Notes: The name Kriging was named for the South African mining engineer Danie G. Krige, who actually developed the method to estimate the distribution of gold under the ground, based on samples from excavations in various points.

## Slide 17: Kriging method
Adding evaluation points can be done by looking at the (expected) error of the response function
Evaluate the system at the point of largest predicted error
Use this additional point in the creation of a new and improved response surface with a smaller error
Kriging is a method of interpolation which is, on average, more accurate than interpolation by simple polynomial
Kriging sees the model as a stochastic process Y(x) = f(x) +Z(x)
Where:
f(x) is the mean (basically the global model of the design space)
Z(x) is the local deviation, such that the Kriging model interpolates the sample points
Notes: More info on Kriging techniques and Kriging mathlab toolbox (DACE) available on the web site of the University of Denmark (www.imm.dtu.dk)

## Slide 18: Kriging method (example)

## Slide 19: Kriging method (example)

## Slide 20: Kriging method (example)

## Slide 21: Optimization using RSM
4. Optimize on the Response Surface Model
This can be done using the fmincon optimization algorithm in Matlab
This only takes a couple of seconds because the evaluation of the RSM is very fast (no simulations required!!!)

## Slide 22: Optimization using RSM
5. Improving the Response Surface Model
  Add the found optimum location as a new sample point
  Reconstruct the RSM by adding the new experiment (computed using the new extra sample point)
  Perform a new optimization
  Repeat this procedure until the solution is converged
Optimum on the RSM
Optimum on the RSM
New derived sample point
Actual design space
RSM
New derived sample point
New performed experiment
Actual design space
RSM
Updated RSM
Old RSM
Actual design space
Old RSM
New RSM
Notes: Then this optimum location is used to improve the quality of the Response Surface Model.
The workflow is evaluated again at the location of the optimum which was found.
The result is added as a new sample point to the RSM, and then the RSM is updated.
With the updated RSM a new optimization can be done.
We will then find a slightly different optimum. When the difference between consecutive iterations has disappeared the solution is considered converged.

## Slide 23: Example of RSM for design space visualization purpose
Notes: The availability of a response surface is useful, not only for optimization but also to the purpose of providing designers with an intuitive visualization of the design space.
Of course, it is not possible to provide usable visualizations of the objective function for more than 2 or 3 design variables

## Slide 24
The variable fidelity optimization approach.
A special use of RSM models

## Slide 25: Optimization
The variable-fidelity optimization approach
Low-fidelity
±3 minutes
High-fidelity
±25 minutes
Notes: This approach called variable-fidelity optimization can be used if there are a low-fidelity and a high-fidelity module in the simulation framework, which describe the same phenomenon.
In this case the low- and high-fidelity parts of the workflow both analyze an aircraft design, but the low-fidelity parts needs about three minutes and the high-fidelity part needs 25 minutes.
The high-fidelity part is of course more accurate but it needs a lot of time.
The variable-fidelity optimization approach uses the low-fidelity model to analyze the aircraft design, but it uses a couple of high-fidelity evaluations to correct the low-fidelity model.
So it can be seen as a way to improve the low-fidelity model such that it approximates the quality of the high-fidelity model.

## Slide 26: Optimization
The variable-fidelity optimization approach
1. Choose sample points for the low-fidelity model (a lot of points) and the high-fidelity model (small number of points)
Low-fidelity
High-fidelity
Notes: First, sample points have to be chosen with the help of Latin Hypercubes.
For the low-fidelity model, a lot of sample points can be chosen, since it is cheap to evaluate.
For the high-fidelity model, only a small number of points is chosen.

## Slide 27: Optimization
The variable-fidelity optimization approach
2. Evaluate the low- and the high-fidelity model at the chosen sample points (Design of Experiments)
Notes: Then a Design of Experiments for the low-fidelity model is done
Again, you can see the sample points and the corresponding responses of the low-fidelity model.

## Slide 28: Optimization
The variable-fidelity optimization approach
3. Build a Response Surface (Kriging) Model of the low-fidelity model
Notes: With the help of the Kriging toolbox a Response Surface of the low-fidelity model is created. No RSM of the High fidelity is generated, however!!

## Slide 29: Optimization
The variable-fidelity optimization approach
4. Determine the difference between the the high-fidelity experiments and the corresponding points measured on the low-fidelity RSM, and use these values to construct a bridge function (again using Kriging)
Notes: Then the differences between the high-fidelity experiments and the corresponding points measured on the low-fidelity RSM are determined. From these differences, a second response surface model is constructed.
This RSM is called the bridge function
The bridge function can be seen as a correction of the low-fidelity model.

## Slide 30: Optimization
The variable-fidelity optimization approach
5. Create the variable-fidelity model by adding the RSM of the low-fidelity model to the bridge function
Notes: In this step the variable-fidelity model is created.
This is done by adding the low-fidelity model and the bridge function together.

## Slide 31: Optimization
The variable-fidelity optimization approach
6. Optimize on the variable-fidelity model
Notes: Now the optimization can be done on the variable-fidelity rather running the whole framework again, with its expensive high fidelity modules.

## Slide 32: Optimization
The variable-fidelity optimization approach
7. Improving the variable-fidelity model
  Perform another high-fidelity evaluation with the found optimum location as sample point
  Reconstruct the bridge function with the extra sample point
  Reconstruct the variable-fidelity model with the updated bridge function
  Perform a new optimization
  Repeat this procedure until the solution is converged
Notes: When the optimum is found, the variable-fidelity model can also be updated.
The high-fidelity model is evaluated at the location of the found optimum. Note that only the HF part of the framework is executed, not the whole framework!
This point is then added as an extra sample point for the bridge function.
Then the variable-fidelity model is updated with the new bridge function.
Then a new optimization can be done. Again, this procedure can be repeated until the solution is converged.

## Slide 33: Optimization example
Optimization of an A320 wing
Two objective functions: MTOM and fuel mass
Three sets of design variables:
  Wing area and aspect ratio
  Wing area, aspect ratio, sweep angle and taper ratio
  Wing area, aspect ratio, sweep angle, taper ratio, root twist, kink twist and tip twist
Constraints:
  TOFL < 2300 m
  LFL < 1900 m
  Wing loading < 600.5
  Climb angle > 2.4º
  Static margin > 0.05
  Mach drag divergence > 0.78
Notes: The two approaches which were described were used on an example problem
The optimization of an A320 configuration
Two objective functions were used: Maximum Take Off Mass and fuel mass
Three sets of design variables were used: in the first optimization the wing area and the aspect ratio were design variables, in the second optimization the entire wing planform could be changed, and in the third set of design variables also the wing twist could be changed.
Furthermore some constraints were implemented.

## Slide 34: Optimization
Results – Optimization with 2 design variables
Classical RSM approach: RSM
Variable Fidelity approach: VFM
Notes: In these pictures you can see the resulting optimized wings if 2 design variables are used.
Two optimizations are actually performed: one using a global RSM build running the whole framework (here called RSM); one using the variable fidelity approach (here called VFM)
The left wing is the wing optimized for Maximum Take Off Mass, the right wing is optimized for minimum fuel.
You can see that the left wing is smaller than the original wing and has a smaller aspect ratio. In this way a decrease of more than a 1000 kg is achieved with respect to the original wing.
The right wing has a larger aspect ratio, such that it is more slender and therefore has a higher lift over drag ratio. In this way the aircraft can fly more efficient and will use less fuel. A fuel decrease of almost 200 kg was achieved for a design mission of 3400 kilometers.
Furthermore one can see that both the optimization approaches converged to the same solution.

## Slide 35: Optimization
Results – Optimization with 4 design variables
Classical RSM approach: RSM
Variable Fidelity approach: VFM
The only case showing significant discrepancy
Notes: These are the results if the entire wing planform can be changed.
The left wing has a lower aspect ratio and lower sweep angle. In this way MTOM is about 1500 kg lower than the original aircraft.
In the right picture you can see the results for minimization of fuel mass. The two approaches have now converged to different solutions. This might be due to the inaccuracy of the response surface models.

## Slide 36: Optimization
Results – Optimization with 7 design variables
Classical RSM approach: RSM
Variable Fidelity approach: VFM
Notes: Finally these two pictures show the optimized wing if also the wing twist is taken into account. Of course the twist cannot actually be displayed in these figures. In this case the two approaches again converged to almost the same solutions.
Again, the minimization of MTOM leads to a low aspect ratio wing, while the minimization of fuel mass leads to a high aspect ratio wing.

## Slide 37: Optimization
Estimation of computation time
Nr. of design variables | Optimization type | Low-fidelity evaluations | High-fidelity evaluations | Nr. of updates | Estimated time [hr]
2 | Full simulation | - | 22 | - | 9.0
 | RSM | - | 12 | 2 | 5.7
 | VFM | 50 | 6 | 3 | 6.1
4 | Full simulation | - | 56 | - | 23.4
 | RSM | - | 24 | 4 | 11.5
 | VFM | 50 | 12 | 4 | 9.3
7 | Full simulation | - | 67 | - | 27.9
 | RSM | - | 42 | 4 | 19.0
 | VFM | 50 | 21 | 5 | 13.2
Classical RSM approach: RSM
Variable Fidelity approach: VFM
Notes: In this table a comparison is made between the various methods.
Three optimization methods are compared:
The regular method, in which an optimizer is just connected to the workflow
Direct optimization of the response surface model of the workflow
A variable-fidelity optimization approach
The use of response surface obviously requires some effort by the designer to make them. Therefore in this estimation it is included how much time it is expected to take to create the response surfaces.
What becomes clear from this picture is that the more design variables are used, the more advantage is offered by the variable-fidelity with respect to the other methods.